Abstract

The KIOT-7000 program is setup to program EEPROMs with serial terminal input. Other features include, support code added / not unit tested, include file EEPROM programming using location “/data/Keeprom1.txt” along with user interface function 4 from the serial terminal. An additional feature is <<run eeprom bank 1-3>>. New hardware features are 5 banks of EEPROM as:

1. EEPROM Bank 1 through 3 – Updated, Program, Copy
2. EEPROM Banks 4 through 5 – Semi permanent app settings and last running conditions

FILE: kiot_7000_r5.ino

// KIOT - 7000 - r5
// March 28, 2023
// Starting to convert routine files to header files
// --- First conversion oledTest3.h
// ==========================================
// KIOT - 7000 - r4
// --- Update process1(), process2(), and process3()
// KIOT - 7000 - r3
// updated with Serial working
// March 23, 2023
// ===========================================================
// KIOT - 7000 - r2
// March 11. 2023
// *** eeprom banks 1-3 verified on new board
// *** OLED verified
// *** serial UI verified
// *** mc23017 verified
//
// Modified board using serial I/O UI
// adding third eeprom bank
// need to setup microSd card and TFT display
// ===========================================================
// KIOT - 6000 r7
// KB Control Works!
// Bus Control
// --- PA0 LED
// --- PA1-PA3 Pb1, Pb2, and Pb3
// --- PA4-PA7 Future Use Bus Control
// --- PB0-PB7 Data I/O Bus
//
// Next tasks - TFT Display and microSD reader/writer
// -----------------------------------------------------------
// Switch control input mode to Serial terminal and status display
// Works for test input to make UI
// Use adafruit mc23107 PA0-7 for control bus
// Use adafruit mc23017 PB0-7 for data I/O bus
//
// Next component TFT screen and microSD port
// ----------------------------------------------------------------------
// Need to review process for using 74165 shift register
// first button gave value of 4
// first and second button pressed gave value of 5
// instead of 1 and 3
// Added - int shiftIn2(...) to read 74165 chip uisng mcp pins
// Need to test KB input
// Compile tests - passed
// =====================================================================
// KB polled test - passed
// Next test - KB entry values
// =====================================================================
// Feb 22, 2023
// Diana Kanecki, DM(ABD), MBA, ACS, Bio. Sci.
// Added eeprom module and test code works!
// Modules: OLED, Adafruite mc23017, eeprom modules
// Last test: keyboard I/O
// =====================================================================
// KIOT-6000 eeprom programmer & specical device control module
// -- oled 128x32 i2c
// -- adafruit mc23017 i2c
// -- both banks eeprom works (remember only byte values)
// to do
// -- command button interface & processing
// -- TFT display port interface and processing
// update from KIOT-5000, feb 22, 2023
// (C) Diana Kanecki 2023, All Rights Reserved for KIOT-6000 coding
/**************************************************************************
This is an example for our Monochrome OLEDs based on SSD1306 drivers

Pick one up today in the adafruit shop!
------> http://www.adafruit.com/category/63_98

This example is for a 128x32 pixel display using I2C to communicate
3 pins are required to interface (two I2C and one reset).

Adafruit invests time and resources providing this open
source code, please support Adafruit and open-source
hardware by purchasing products from Adafruit!

Written by Limor Fried/Ladyada for Adafruit Industries,
with contributions from the open source community.
BSD license, check license.txt for more information
All text above, and the splash screen below must be
included in any redistribution.
**************************************************************************/

#include <SPI.h>
#include <Wire.h>
#include <Adafruit_GFX.h>
#include <Adafruit_SSD1306.h>
// ok to include only the one needed
// both included here to make things simple for example

#include "oledTest3.h"
#include "eeprom1.h"
#include "mcp23017support1.h"
#include "Support8255-1.h"
#include "spiffsSupport1.h"

// ============================
// KIOT-6000 section
// ============================
int count =0;
int loopCount = 0;
//#define CEPin 1 // PA1 on mc23017
//#define QHPin 2 // PA2
//#define ClkPin 3 // PA3
//#define KbPin 4 // PA4

void setup() {
Serial.begin(9600);

setupMCP23017();
setupEEPROM();

// SSD1306_SWITCHCAPVCC = generate display voltage from 3.3V internally
if(!display.begin(SSD1306_SWITCHCAPVCC, SCREEN_ADDRESS)) {
Serial.println(F("SSD1306 allocation failed"));
for(;;); // Don't proceed, loop forever
}

// Show initial display buffer contents on the screen --
// the library initializes this with an Adafruit splash screen.
display.display();
delay(2000); // Pause for 2 seconds

// Clear the buffer
display.clearDisplay();

// Draw a single pixel in white
display.drawPixel(10, 10, SSD1306_WHITE);

// Show the display buffer on the screen. You MUST call display() after
// drawing commands to make them visible on screen!
display.display();
delay(2000);
// display.display() is NOT necessary after every single drawing command,
// unless that's what you want...rather, you can batch up a bunch of
// drawing operations and then update the screen all at once by calling
// display.display(). These examples demonstrate both approaches...

testdrawline(); // Draw many lines

testdrawrect(); // Draw rectangles (outlines)

testfillrect(); // Draw rectangles (filled)

testdrawcircle(); // Draw circles (outlines)

testfillcircle(); // Draw circles (filled)

testdrawroundrect(); // Draw rounded rectangles (outlines)

testfillroundrect(); // Draw rounded rectangles (filled)

testdrawtriangle(); // Draw triangles (outlines)

testfilltriangle(); // Draw triangles (filled)

testdrawchar(); // Draw characters of the default font

testdrawstyles(); // Draw 'stylized' characters

testscrolltext(); // Draw scrolling text

testdrawbitmap(); // Draw a small bitmap image

// Invert and restore display, pausing in-between
display.invertDisplay(true);
delay(1000);
display.invertDisplay(false);
delay(1000);

//testanimate(logo_bmp, LOGO_WIDTH, LOGO_HEIGHT); // Animate bitmaps
}

int shiftIn2(int dataPin, int clkPin, int bitOrder){
int value =0;
int i;

for (i=0; i<8; i++){
mcp.digitalWrite(clkPin, HIGH);
delay(500);

if (bitOrder == LSBFIRST)
value |= mcp.digitalRead(dataPin) << i;
else
value |= mcp.digitalRead(dataPin) << (7-i);
mcp.digitalWrite(clkPin, LOW);
delay(500);
}

return value;

}

int sRdInt(){

bool kbReady = false;
int count = 0;
int val = 0xFF;
String input1;

while(Serial.available() == 0){ }
input1=Serial.readString();
val = input1.toInt();

return val;
}

void doProcess1(){
// Upload data to EEPROM bank 1-3
// Updated March 27, 2023
// (C) Diana Kanecki, 2026, All Rights Reserve

int bankID;
int lineCode;
int val[9];
int startAddr;
String dataIn;
char dataBuf[256];
int dlen;

Serial.println(" *** Process 1");
Serial.println(" --- UPLOAD Data to EEPROM Bank");
Serial.println();
Serial.print("Enter Bank ID?");
bankID = sRdInt();
Serial.print(" Bank ID Entered (1-3):");
Serial.println(bankID);

Serial.print("Enter staring address?");
startAddr = sRdInt();
Serial.print(" Starting Address is:");
Serial.println(startAddr,HEX);

lineCode =0;
while (lineCode != 9999){
Serial.print("Enter Line Cmd?");
lineCode = sRdInt();
Serial.print(" Line cmd is:");
Serial.println(lineCode);

switch(lineCode){
case 1: // upload data
Serial.print(lineCode);
Serial.print(startAddr,HEX);
Serial.print(" >");

while (Serial.available() == 0) {}
dataIn = Serial.readString();
Serial.println(dataIn);

dataIn.toCharArray(dataBuf,dataIn.length()+1);
for (int k=0; k<=7; k++)
val[k]=-1;

sscanf(dataBuf,"%d %d %d %d %d %d %d %d",
&val[0],&val[1],&val[2],&val[3],
&val[4],&val[5],&val[6],&val[7]);

Serial.println("Data Entered");
for (int i=0; i<=7; i++){
Serial.print(val[i]);
Serial.print(" ");
}
Serial.println();
Serial.println();

for (int k=0; k<=7; k++){
if (val[k]!=-1){
int diskId = disk1 + (bankID-1);
writeEEPROM(diskId,startAddr,val[k]);
startAddr++;
}
}
break;
case 2: // process comment
Serial.print("2 >");
while (Serial.available() == 0) {}
dataIn = Serial.readString();
Serial.println(dataIn);
break;
}
}
}

void doProcess2(){
// copy data from one EEPROM bank to another
// Started March 27, 2023
// (C) Diana Kanecki, 2023, All Rights Reserved
Serial.println(" *** Copy One EEPROM to Another");

int bankID, bankID2;
int startAddr, stopAddr;
String inpLine;
char dataBuf[256];
int dataLen;
int d1;
int rdBank;
int wrBank;

Serial.print("Enter Start Bank (1-3) & Copy Bank (1-3)?");
inpLine = Serial.readString();
inpLine.toCharArray(dataBuf,inpLine.length()+1);
sscanf(dataBuf,"%d %d", &startAddr, &stopAddr);

Serial.print("start ->");
Serial.print(startAddr,HEX);
Serial.print(" stop->");
Serial.println(stopAddr,HEX);

for (int i=startAddr; i<=stopAddr; i++){
rdBank = disk1 +(bankID-1);
wrBank = disk1 +(bankID2-1);

d1= readEEPROM(rdBank,i);
writeEEPROM(wrBank,i,d1);

if (((i-startAddr) % 1024) == 0)
Serial.print("*");
}
Serial.println();
Serial.println("*** Copy Completed ***");
}

void doProcess3(){
// Display EEPROM data in DDT format of CP/M
// Started March 26, 2023
// (C) 2023 Diana Kanecki, All Rights Reserved

int lineCode;
int data1[9];
int bankID;
int rdBank;
int d1[9];
String inpLine;
char dataBuf[256];
int dataLen;
int addr1;

Serial.println(" *** Display EEPROM Data");
Serial.print("Bank ID(1-3)?");
inpLine = Serial.readString();
inpLine.toCharArray(dataBuf,inpLine.length()+1);

sscanf(dataBuf,"%d", &bankID);
rdBank = disk1 + (bankID-1);

Serial.print("Enter startAddr?");
inpLine = Serial.readString();
inpLine.toCharArray(dataBuf,inpLine.length()+1);
sscanf(dataBuf,"%d",&addr1);
do {
for (int k=0; k<=7; k++){

for (int i=0; i<=7;i++)
d1[i] = readEEPROM(rdBank,addr1+i);

Serial.print(addr1,HEX);
Serial.print(">");
for (int i=0; i<=7; i++){
Serial.print(d1[i],HEX);
Serial.print(" ");
}
Serial.println();
addr1 += 8;
}

Serial.print("Enter 9999 to stop display?");
inpLine=Serial.readString();
inpLine.toCharArray(dataBuf,inpLine.length()+1);
sscanf(dataBuf,"%d",&lineCode);
}
while (lineCode != 9999);
}

void doProcess4() {
Serial.println(" ** doProcess 4");
}

void test4(){
int val;

Serial.println("=== KIOT-7000\n");
Serial.println("(1) Upload Data to EEPROM bank");
Serial.println("(2) Copy Data from EEPROM bank");
Serial.println("(3) Display EEPROM data");
Serial.print("Enter Option: ");

val = sRdInt();

Serial.println();
Serial.print("Value Entered: ");
Serial.println(val);
delay(2000);

switch(val){
case 1:
doProcess1();
break;
case 2:
doProcess2();
break;
case 3:
doProcess3();
break;
case 4:
doProcess4();
break;
} // end case

}

void loop() {

byte val;
int kbStatus;
int kbCode;
String inStr;
int inKey;
bool debug=false;

Serial.println();
Serial.println(" === KIOT-7000 Dev System r2");
Serial.println();

display.setTextSize(1); // Normal 1:1 pixel scale
display.setTextColor(SSD1306_WHITE); // Draw white text
display.setCursor(0, 0); // Start at top-left corner
display.cp437(true); // Use full 256 char 'Code Page 437' font
display.clearDisplay();
display.print("KIOT-6K r7-");
// display.print(" loop ");
display.println(loopCount);
display.display();

// temporarily block out until chip wired
mcp.digitalWrite(LED_PIN, HIGH);
delay(1000);

// delay(1000);

// temporarily blocked out until chip wired
mcp.digitalWrite(LED_PIN, LOW);
// delay(1000);
// test2(); // qc passed
// test3(); // qc passed

test4();
delay(2000);

loopCount++;
}

void test2(){
int val;

// write bank 1
writeEEPROM(disk1,address,123);
display.print("... wr EEP");
// display.display();

val = readEEPROM(disk1,address);
display.print(" v=");
display.println(val);
display.display();

// write bank 2
writeEEPROM(disk2,address,21);
display.print("... wr EEP2");

val = readEEPROM(disk2,address);
display.print(" v=");
display.println(val);
display.display();

// write bank 3
writeEEPROM(disk3,address,33);
display.print("... wr EEP3");

val = readEEPROM(disk3,address);
display.print(" v=");
display.println(val);
display.display();

}

void test3(){
bool kbReady;
int count;
int kbCode;
int inKey;
String inStr;
bool debug = true;

display.println("Press Btn/Key");
display.display();

Serial.println("Press Key to Continue");
delay(500);
kbReady = false;
count =0;
kbCode=0;

while((!kbReady) && (count <20) ){
if (Serial.available() !=0 )
{
kbReady=true;
inStr = Serial.readString();
}
else
inStr = "***";
inKey = mcp.digitalRead(pb1);
kbCode = inKey;

inKey = mcp.digitalRead(pb2);
kbCode = (inKey << 1) + kbCode;

inKey = mcp.digitalRead(pb3);
kbCode = (inKey << 2) + kbCode;

kbReady = kbReady || (kbCode!=0);

if (debug){
display.setCursor(0, 0);
display.clearDisplay();
display.print("kbCode ");
display.println(kbCode);
display.print("kbStatus ");
display.println(kbReady);
display.display();

Serial.print("kbCode = ");
Serial.println(kbCode);
Serial.print("kbStatus = ");
Serial.println(kbReady);
Serial.println();
//delay(2000);
}
count++;
delay(500);
}

display.setCursor(0, 0);
display.clearDisplay();
display.display();

if (debug) {
display.print("---kbReady ");
display.println(kbReady);
Serial.print("--- kbReady ");
Serial.println(kbReady);
}
if (kbCode !=0){
display.print("BTN Pressed ");
display.println(kbCode);
display.display();
Serial.print("BTN Pressed ");
Serial.println(kbCode);
delay(2000);
}
else {
Serial.println(" Key Pressed:");
Serial.print (" Str:");
Serial.println(inStr);
Serial.println();

display.println("Sel Key:");
display.println(inStr);
display.display();
delay(2000);
};

}

FILE: oledTest3.h

// ********************************
// *** OLED Test Routines
// *** March 26, 2023
// ********************************

// ===========================
// OLED section
// ===========================
#define SCREEN_WIDTH 128 // OLED display width, in pixels
#define SCREEN_HEIGHT 32 // OLED display height, in pixels

// Declaration for an SSD1306 display connected to I2C (SDA, SCL pins)
// The pins for I2C are defined by the Wire-library.
// On an arduino UNO: A4(SDA), A5(SCL)
// On an arduino MEGA 2560: 20(SDA), 21(SCL)
// On an arduino LEONARDO: 2(SDA), 3(SCL), ...
#define OLED_RESET -1 // Reset pin # (or -1 if sharing Arduino reset pin)
#define SCREEN_ADDRESS 0x3C ///< See datasheet for Address; 0x3D for 128x64, 0x3C for 128x32
Adafruit_SSD1306 display(SCREEN_WIDTH, SCREEN_HEIGHT, &Wire, OLED_RESET);

#define NUMFLAKES 10 // Number of snowflakes in the animation example

#define LOGO_HEIGHT 16
#define LOGO_WIDTH 16
static const unsigned char PROGMEM logo_bmp[] =
{ 0b00000000, 0b11000000,
0b00000001, 0b11000000,
0b00000001, 0b11000000,
0b00000011, 0b11100000,
0b11110011, 0b11100000,
0b11111110, 0b11111000,
0b01111110, 0b11111111,
0b00110011, 0b10011111,
0b00011111, 0b11111100,
0b00001101, 0b01110000,
0b00011011, 0b10100000,
0b00111111, 0b11100000,
0b00111111, 0b11110000,
0b01111100, 0b11110000,
0b01110000, 0b01110000,
0b00000000, 0b00110000 };

// temporarily block out until chip wired

void testdrawline() {
int16_t i;

display.clearDisplay(); // Clear display buffer

for(i=0; i<display.width(); i+=4) {
display.drawLine(0, 0, i, display.height()-1, SSD1306_WHITE);
display.display(); // Update screen with each newly-drawn line
delay(1);
}
for(i=0; i<display.height(); i+=4) {
display.drawLine(0, 0, display.width()-1, i, SSD1306_WHITE);
display.display();
delay(1);
}
delay(250);

display.clearDisplay();

for(i=0; i<display.width(); i+=4) {
display.drawLine(0, display.height()-1, i, 0, SSD1306_WHITE);
display.display();
delay(1);
}
for(i=display.height()-1; i>=0; i-=4) {
display.drawLine(0, display.height()-1, display.width()-1, i, SSD1306_WHITE);
display.display();
delay(1);
}
delay(250);

display.clearDisplay();

for(i=display.width()-1; i>=0; i-=4) {
display.drawLine(display.width()-1, display.height()-1, i, 0, SSD1306_WHITE);
display.display();
delay(1);
}
for(i=display.height()-1; i>=0; i-=4) {
display.drawLine(display.width()-1, display.height()-1, 0, i, SSD1306_WHITE);
display.display();
delay(1);
}
delay(250);

display.clearDisplay();

for(i=0; i<display.height(); i+=4) {
display.drawLine(display.width()-1, 0, 0, i, SSD1306_WHITE);
display.display();
delay(1);
}
for(i=0; i<display.width(); i+=4) {
display.drawLine(display.width()-1, 0, i, display.height()-1, SSD1306_WHITE);
display.display();
delay(1);
}

delay(2000); // Pause for 2 seconds
}

void testdrawrect(void) {
display.clearDisplay();

for(int16_t i=0; i<display.height()/2; i+=2) {
display.drawRect(i, i, display.width()-2*i, display.height()-2*i, SSD1306_WHITE);
display.display(); // Update screen with each newly-drawn rectangle
delay(1);
}

delay(2000);
}

void testfillrect(void) {
display.clearDisplay();

for(int16_t i=0; i<display.height()/2; i+=3) {
// The INVERSE color is used so rectangles alternate white/black
display.fillRect(i, i, display.width()-i*2, display.height()-i*2, SSD1306_INVERSE);
display.display(); // Update screen with each newly-drawn rectangle
delay(1);
}

delay(2000);
}

void testdrawcircle(void) {
display.clearDisplay();

for(int16_t i=0; i<max(display.width(),display.height())/2; i+=2) {
display.drawCircle(display.width()/2, display.height()/2, i, SSD1306_WHITE);
display.display();
delay(1);
}

delay(2000);
}

void testfillcircle(void) {
display.clearDisplay();

for(int16_t i=max(display.width(),display.height())/2; i>0; i-=3) {
// The INVERSE color is used so circles alternate white/black
display.fillCircle(display.width() / 2, display.height() / 2, i, SSD1306_INVERSE);
display.display(); // Update screen with each newly-drawn circle
delay(1);
}

delay(2000);
}

void testdrawroundrect(void) {
display.clearDisplay();

for(int16_t i=0; i<display.height()/2-2; i+=2) {
display.drawRoundRect(i, i, display.width()-2*i, display.height()-2*i,
display.height()/4, SSD1306_WHITE);
display.display();
delay(1);
}

delay(2000);
}

void testfillroundrect(void) {
display.clearDisplay();

for(int16_t i=0; i<display.height()/2-2; i+=2) {
// The INVERSE color is used so round-rects alternate white/black
display.fillRoundRect(i, i, display.width()-2*i, display.height()-2*i,
display.height()/4, SSD1306_INVERSE);
display.display();
delay(1);
}

delay(2000);
}

void testdrawtriangle(void) {
display.clearDisplay();

for(int16_t i=0; i<max(display.width(),display.height())/2; i+=5) {
display.drawTriangle(
display.width()/2 , display.height()/2-i,
display.width()/2-i, display.height()/2+i,
display.width()/2+i, display.height()/2+i, SSD1306_WHITE);
display.display();
delay(1);
}

delay(2000);
}

void testfilltriangle(void) {
display.clearDisplay();

for(int16_t i=max(display.width(),display.height())/2; i>0; i-=5) {
// The INVERSE color is used so triangles alternate white/black
display.fillTriangle(
display.width()/2 , display.height()/2-i,
display.width()/2-i, display.height()/2+i,
display.width()/2+i, display.height()/2+i, SSD1306_INVERSE);
display.display();
delay(1);
}

delay(2000);
}

void testdrawchar(void) {
display.clearDisplay();

display.setTextSize(1); // Normal 1:1 pixel scale
display.setTextColor(SSD1306_WHITE); // Draw white text
display.setCursor(0, 0); // Start at top-left corner
display.cp437(true); // Use full 256 char 'Code Page 437' font

// Not all the characters will fit on the display. This is normal.
// Library will draw what it can and the rest will be clipped.
for(int16_t i=0; i<256; i++) {
if(i == '\n') display.write(' ');
else display.write(i);
}

display.display();
delay(2000);
}

void testdrawstyles(void) {
display.clearDisplay();

display.setTextSize(1); // Normal 1:1 pixel scale
display.setTextColor(SSD1306_WHITE); // Draw white text
display.setCursor(0,0); // Start at top-left corner
display.println(F("Hello, world!"));

display.setTextColor(SSD1306_BLACK, SSD1306_WHITE); // Draw 'inverse' text
display.println(3.141592);

display.setTextSize(2); // Draw 2X-scale text
display.setTextColor(SSD1306_WHITE);
display.print(F("0x")); display.println(0xDEADBEEF, HEX);

display.display();
delay(2000);
}

void testscrolltext(void) {
display.clearDisplay();

display.setTextSize(2); // Draw 2X-scale text
display.setTextColor(SSD1306_WHITE);
display.setCursor(10, 0);
display.println(F("scroll"));
display.display(); // Show initial text
delay(100);

// Scroll in various directions, pausing in-between:
display.startscrollright(0x00, 0x0F);
delay(2000);
display.stopscroll();
delay(1000);
display.startscrollleft(0x00, 0x0F);
delay(2000);
display.stopscroll();
delay(1000);
display.startscrolldiagright(0x00, 0x07);
delay(2000);
display.startscrolldiagleft(0x00, 0x07);
delay(2000);
display.stopscroll();
delay(1000);
}

void testdrawbitmap(void) {
display.clearDisplay();

display.drawBitmap(
(display.width() - LOGO_WIDTH ) / 2,
(display.height() - LOGO_HEIGHT) / 2,
logo_bmp, LOGO_WIDTH, LOGO_HEIGHT, 1);
display.display();
delay(1000);
}

#define XPOS 0 // Indexes into the 'icons' array in function below
#define YPOS 1
#define DELTAY 2

void testanimate(const uint8_t *bitmap, uint8_t w, uint8_t h) {
int8_t f, icons[NUMFLAKES][3];

// Initialize 'snowflake' positions
for(f=0; f< NUMFLAKES; f++) {
icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
icons[f][YPOS] = -LOGO_HEIGHT;
icons[f][DELTAY] = random(1, 6);
Serial.print(F("x: "));
Serial.print(icons[f][XPOS], DEC);
Serial.print(F(" y: "));
Serial.print(icons[f][YPOS], DEC);
Serial.print(F(" dy: "));
Serial.println(icons[f][DELTAY], DEC);
}

for(;;) { // Loop forever...
display.clearDisplay(); // Clear the display buffer

// Draw each snowflake:
for(f=0; f< NUMFLAKES; f++) {
display.drawBitmap(icons[f][XPOS], icons[f][YPOS], bitmap, w, h, SSD1306_WHITE);
}

display.display(); // Show the display buffer on the screen
delay(200); // Pause for 1/10 second

// Then update coordinates of each flake...
for(f=0; f< NUMFLAKES; f++) {
icons[f][YPOS] += icons[f][DELTAY];
// If snowflake is off the bottom of the screen...
if (icons[f][YPOS] >= display.height()) {
// Reinitialize to a random position, just off the top
icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
icons[f][YPOS] = -LOGO_HEIGHT;
icons[f][DELTAY] = random(1, 6);
}
}
}
}

FILE: eeprom.h

// EEPROM support routine 1
// March 28, 2023
// ====================================
#include <SPI.h>
#include <Wire.h>

// ===================================
// eeprom section
// ===================================
#define disk1 0x50 // addr of eeprom chip
#define disk2 0x51 // addr of bank 2 of eeprom
#define disk3 0x52 // aadr of bank 3 of eeprom

unsigned int address=0;

void setupEEPROM(){
Wire.begin();
}

void writeEEPROM(int deviceaddress, unsigned int eeaddress, byte data){
Wire.beginTransmission(deviceaddress);
Wire.write((int)(eeaddress >> 8)); // MSB
Wire.write((int)(eeaddress & 0xFF)); // LSB
Wire.write(data);
Wire.endTransmission();
delay(5);
}

byte readEEPROM(int deviceaddress, unsigned int eeaddress){
byte rdata = 0xFF;

Wire.beginTransmission(deviceaddress);
Wire.write((int)(eeaddress >> 8)); // MSB
Wire.write((int)(eeaddress & 0xFF)); // LSB
Wire.endTransmission();

Wire.requestFrom(deviceaddress,1);
if (Wire.available()) rdata = Wire.read();

return rdata;

}

FILE: mcp23017support1.h

// ==========================================
// mcpSupport 1 - March 27, 2023
// ==========================================

#include <Adafruit_MCP23X08.h>
#include <Adafruit_MCP23X17.h>

// ===================================
// mc23017 section
// ===================================
// uncomment appropriate line
//Adafruit_MCP23X08 mcp;
Adafruit_MCP23X17 mcp;

#define LED_PIN 0 // MCP23XXX pin LED is attached to

// only used for SPI
#define CS_PIN 6

#define pb1 1 // PA2
#define pb2 2 // PA3
#define pb3 3 // PA4
bool kbReady = false;

#define pD0 8 // PB0
#define pD7 15 // PB7

void writeAFPort2(int data){
int d1;

for (int i=0;i<=7;i++){
mcp.pinMode(pD0+i, OUTPUT);
d1 = data & 0x1;
data = data >> 1;
mcp.digitalWrite(pD0+i, d1);
}
}

int readAFPort2(){
int d1;
int data =0;

for (int i=0;i<=7;i++){
mcp.pinMode(pD0+i, INPUT);
d1 = mcp.digitalRead(pD0+i);
data = data + d1;
data - data << 1;
}

return data;
}

// temporarily block out until chip wired
void setupMCP23017() {
// Serial.begin(9600);
//while (!Serial);
Serial.println("MCP23xxx Blink Test!");

// uncomment appropriate mcp.begin
if (!mcp.begin_I2C()) {
//if (!mcp.begin_SPI(CS_PIN)) {
Serial.println("Error.");
while (1);
}

// configure pin for output
mcp.pinMode(LED_PIN, OUTPUT);
//mcp.digitalWrite( CEPin, LOW);
//mcp.digiINPU)

mcp.pinMode(pb1, INPUT);
mcp.pinMode(pb2, INPUT);
mcp.pinMode(pb3, INPUT);
}

FILE: Support8255-1.h

// ========================================
// 8255 chip support
// (C) Diana Kanecki, 2023 All Rights Reserved
// March 30, 2023
// ========================================

// Adafruit MC23017 GPIO settings
#define LED1 0
#define A0x 1
#define A1x 2
#define WRx 3
#define RDx 4
#define ctrl11 5
#define ctrl12 6
#define ctrl13 7

#define portA 0
#define portB 1
#define portC 2
#define CSR 4

#define outDB0 8
#define outDB1 9
#define outDB2 10
#define outDB3 11
#define outDB4 12
#define outDB5 13
#define outDB6 14
#define outDB7 15

void setCSR(){
mcp.digitalWrite(A0x,HIGH);
mcp.digitalWrite(A1x,HIGH);

for (int i=0; i<=7; i++) {
mcp.digitalWrite((outDB0+i), LOW);
}

mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);
}

void setup8255(){
mcp.pinMode(WRx,OUTPUT);
mcp.pinMode(A0x,OUTPUT);
mcp.pinMode(A1x,OUTPUT);
mcp.pinMode(RDx,OUTPUT);

for (int i=0; i<=7; i++)
mcp.pinMode((outDB0+i),OUTPUT);

mcp.digitalWrite(RDx,HIGH);
mcp.digitalWrite(WRx,HIGH);
setCSR();

// Send test data to portA
mcp.digitalWrite(outDB1,HIGH);
mcp.digitalWrite(outDB2,HIGH);
mcp.digitalWrite(A1x,LOW);
mcp.digitalWrite(A0x,LOW);
mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);

// Send test data to port B
mcp.digitalWrite(outDB0,HIGH);
mcp.digitalWrite(outDB1,HIGH);
mcp.digitalWrite(A1x,LOW);
mcp.digitalWrite(A0x,HIGH);
mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);
}

void writePortA(int data1){
volatile int tmp;

for (int i=0; i<=7; i++)
mcp.pinMode((outDB0+i),OUTPUT);

for (int i=0; i<=7; i++){
tmp = data1 & 1;
mcp.digitalWrite((outDB0+i),tmp);
data1 = data1 >> 1;
}

mcp.digitalWrite(A1x,LOW);
mcp.digitalWrite(A0x,LOW);
mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);

}

void writePortB( int data1){
volatile int tmp;

for (int i=0;i<=7;i++)
mcp.pinMode((outDB0+i),OUTPUT);

for (int i=0; i<=7; i++){
tmp = data1 & 1;
mcp.digitalWrite((outDB0+i),tmp);
data1 = data1 >> 1;
}

mcp.digitalWrite(A1x,LOW);
mcp.digitalWrite(A0x,HIGH);
mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);

}

void setRegister(int data1){
volatile int tmp;

tmp = data1 & 1;
mcp.digitalWrite(A0x,tmp);
data1 = data1 >> 1;
tmp = data1 & 1;
mcp.digitalWrite(A1x,tmp);
}

void writePortX(int regNum, int data1){
volatile int tmp;

setRegister(regNum);

for (int i=0; i<=7; i++)
mcp.pinMode((outDB0+i),OUTPUT);

for (int i=0; i<=7; i++){
tmp = data1 & 1;
mcp.digitalWrite((outDB0+i),tmp);
data1 = data1 >> 1;
}

mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);
}

int rdPortX(int regNum){
volatile int data1 = 0;
volatile int tmp;

setRegister(regNum);
for (int i=0; i<=7; i++)
mcp.pinMode((outDB0+i),INPUT);

for (int i=7; i>=0; i--){
tmp = mcp.digitalRead((outDB0+i));
data1 = data1 + tmp;
data1 = data1 << 1;
}

mcp.digitalWrite(WRx,LOW);
delay(10);
mcp.digitalWrite(WRx,HIGH);

return data1;
}

FILE: spiffsSupport1.h

// ======================================================
// File Support 1 System 1.0
// April 4, 2023
// (C) Diana Kanecki 2023, All Rights Reseved (for my parts)

#include "FS.h"

void setupSPIFFS(){
// mount and check file system
bool ok = SPIFFS.begin();
if (ok) {
Serial.println("SPIFFS Initialized Successfully");
}
else {
Serial.println("*** SPIFFS Not Initialized");
}
}

void loopTestSPIFFS(){
// open log file
File file = SPIFFS.open("/log.txt","a");
if (!file){
Serial.println("*** FILE Open Failed");
}
// write sample data

file.println("Sample Data Line 1");
file.println("Sample - Line 2");

// close file
file.close();
}

void fileOpen(File file, String fname){
// Started April 4, 2023
// (C) Diana Kanecki, All Rights Reserved
file = SPIFFS.open(fname,"a");
if (!file)
Serial.println("*** File OPEN Failed");
}

void fileClose(File file){
// Started April 4, 2023
// (C) Diana Kanecki, All Rights Reserved
file.close();
}